Vibration Analyzer/Data Collector 903

Manuals Download:   903    /   PM Software    /   Diagnosis Software

Software Download:   PM Software 2.0 (18Mbytes)

Features:

· On-site FFT spectrum analysis and waveform display

· Full featured data collector for predictive maintenance

· Optional balancing module for 1 and 2-planes field balancing with influence coefficient method

· DOS and Windows-based PC software with functions of maintenance database management, trend analysis, various spectrum analysis, waveform analysis, time-domain diagnosis, bearing and gear box diagnosis

· Large display LCD screen , 128×112 pixels

· Menu-driven with English prompts

· Measure vibration displacement, velocity, acceleration and acceleration envelope with a single transducer

· Large memory for 270 data sets (include route, four vibration characteristic value, a 100-line spectrum, condition code for visual inspection,process parameter)

· Spectrum comparison function.

· Small size, handheld and rugged design.

Specifications:

·Input signal: accelerometer, and voltage

·Amplitude ranges & Frequency Response

Displacement 1 - 5000µm peak-peak 10 - 500 Hz

Velocity 0.1 - 200mm/s true RMS 10 - 1000 Hz

Acceleration 0.1 - 250m/s2 peak 10 - 10000 Hz

Envelope 0.1 - 20m/s2 true RMS 5 - 1000Hz from 15-40Hz

Voltage 0.1 - 20V peak-peak 10 - 1000 Hz

·Amplitude spectrum analysis: 100 / 400 Lines, hanning windowed

·Frequency range of spectrum analysis: 100, 200, 500, 1k, 2k, 5k, 10kHz

·Data storage: 62 1024-point time waveforms and 350 data sets

·Notepad: 10 condition codes for visual inspection

·Output: RS232C for communication with PC

·Power: Ni-MH rechargeable battery for 8 hours continuous operation, low battery

warning

·Operating Environment: 0-50ºC, 90% humidity non-condensing

·Rotating speed measurement with photocell sensor

·Dynamic Range: 60dB with 48dB adjustable gain range

·Anti-aliasing filter: 8th order elliptic lowpass

·Dimensions: 21×13×4cm; weight: 1.2 kg